## Slide 1: Performance Analysis of Interconnection Networks with Source-Code Attribution
Adarsh Yoga and Milind Chabbi
14 August 2017

## Slide 2: Motivation
State-of-the-art developer tools for performance analysis measure in-node, CPU-only metrics
Interconnection networks are a significant fraction of execution time
  Data movement cost exceeds cost of computing on the data
Network remains a black-box from a developer’s perspective

## Slide 3: Challenge of Data Movement
Node
Node
Node
Node
Node
Node
.
.
.
.
.
.
Switch
Switch
Switch
Switch
NIC
NIC
NIC
NIC
NIC
NIC
Bottlenecks can occur in,
  Local NIC
  Switch hops
  Destination NIC
  Forward/return path
  Intra/Inter job interference
  Topology/routing algorithms
  Hardware provisioning

## Slide 4: Challenge of Data Movement
Node
Node
Node
Node
Node
Node
.
.
.
.
.
.
Switch
Switch
Switch
Switch
Bottlenecks can occur in,
  Local NIC
  Switch hops
  Destination NIC
  Forward/return path
  Intra/Inter job interference
  Topology/routing algorithms
  Hardware provisioning
NIC
NIC
NIC
NIC
NIC
NIC

## Slide 5: Need Detailed Insight
Node
Node
Node
Node
Node
Node
.
.
.
.
.
.
Switch
Switch
Switch
Switch
Detailed insight into the data movement and consequence on application source code
Need telemetry of,
  Congested switches
  Path traversed and its effect on latency
  Delays associated with link-level credits
  Delays introduced by destination node hardware/software
NIC
NIC
NIC
NIC
NIC
NIC

## Slide 6: Refactor Software
Node
Node
Node
Node
Node
Node
.
.
.
.
.
.
Switch
Switch
Switch
Switch
Many performance problems can be fixed by simple refactor of application source code
For example, if lock release is frequently affected by network delays, then use higher priority VC for lock release
NIC
NIC
NIC
NIC
NIC
NIC

## Slide 7: Our Work
Goal: Identify performance problems that occur in the network and co-relate to application source code.
Approach:
Track the movement of packets through the network
Collect performance metrics about the packets at every step
Attribute metrics to application source code
  Aid application developer with rich visualization and automatic data ingestion

## Slide 8: Overview
Input MPI program
Performance Stats Collection
Path Construction
Performance Visualization
Output graphs

## Slide 9: Performance Stats Collection
Tracking all messages/packets is expensive
  Use sampling to randomly/smartly select messages to monitor
A single bit (PM bit) in packet header used to track packets that are selected to be monitored (marked packet)
  Advantages: Unsynchronized data collection in concurrent autonomous many-component systems
  Hop-by-hop path synchronous metrics
Propose extensions to network components to enable efficient performance stats collection for every marked packet

## Slide 10: Node-side Stats Collection
Software profiler selects a message at random and marks it to be tracked
Both source and destination nodes collect stats for a marked message
Stats: source node id, destination node id, message id, departure time/arrival time, application side calling context
Source Node
Dest Node
Switch
Switch
Switch
Switch
Node log
Node log

## Slide 11: NIC and Network-side Stats
For a marked message, NIC hardware selects one among N packets and sets PM bit in header
  Could select more than one packet
NIC and switch collect stats for the packet if PM bit set
Stats: output port, arrival time, departure time, buffer size, credits
Source Node
Dest Node
Switch
Switch
Switch
Switch
Nic log
Nic log
NIC
NIC
Switch log
Switch log

## Slide 12: Hardware Extensions
Goal is to minimize time spent in logging performance stats at NIC and Switch
Log to a on-chip circular bounded buffer and a independent hardware component periodically drains logs from the buffer
NIC
DRAINER
NODE
SWITCH
DRAINER
SWITCH
DRAINER
NIC and switch add logs to the end of buffer
Drainer periodically reads from buffer and write to a collection server (NFS mounted file)

## Slide 13: Implementation – SST/Macro
Simulator for large-scale interconnection networks
Emphasize coarse-grain approximations over accuracy
Pros:
  Modular design; can be easily extended with additional network components
  Perform analysis of varying network design parameters like machine models, packet flow models and topologies
  Model realistic applications using Skeletons – MPI communication with limited computation
Notes: It permits the coarse-grained study of distributed-memory applications.
For large, system-level experiments with thousands of network endpoints, high-accuracy cycle-accurate simulation is not possible, or at least not convenient. Simulation requires coarse-grained approximations to be practical.

## Slide 14: SST/Macro for Stats Collection
Extended to Node module implementation to
  randomly select messages to monitor
  Log node side performance statistics
Implemented the Drainer as sub-component of the Node and Switch module and added buffers to hold the logs
Extended the Nic and the Switch module to collect performance statistics and write to the buffers
Collect machine configuration information that shows how nodes and switches are connected
Output: Set of log files containing performance statistics for monitored packets and machine configuration information
Notes: It permits the coarse-grained study of distributed-memory applications.
For large, system-level experiments with thousands of network endpoints, high-accuracy cycle-accurate simulation is not possible, or at least not convenient. Simulation requires coarse-grained approximations to be practical.

## Slide 15: Overview
Input MPI program
Performance Stats Collection
Path Construction
Performance Visualization
Output graphs

## Slide 16: Path Construction
Post mortem pass to identify the path taken by each logged packet and compute delay (and other metrics) at each step
Read all the logs into memory in parallel
Use unordered maps to store per-component configuration information; indexed by port number
Use ordered maps to store per-component performance statistics information; indexed by the time the packet arrived at the component
Notes: It permits the coarse-grained study of distributed-memory applications.
For large, system-level experiments with thousands of network endpoints, high-accuracy cycle-accurate simulation is not possible, or at least not convenient. Simulation requires coarse-grained approximations to be practical.

## Slide 17: Path Construction Algorithm
…
0,i, …,port,dep time
…
Node log 0
For each log entry of a packet originating for the same node
Obtain next hop log using output port and config info
…
0, …,port,dep time
…
Switch log 0
Use departure time + delta to find a range of entries. Then use src id, dest id, message/packet id to find exact entry
……
…..
Node log i
…
…
…
0,i, …,port,dep time
…
Node log n
……
Repeat the same process for all n Nodes in parallel
Notes: It permits the coarse-grained study of distributed-memory applications.
For large, system-level experiments with thousands of network endpoints, high-accuracy cycle-accurate simulation is not possible, or at least not convenient. Simulation requires coarse-grained approximations to be practical.

## Slide 18: Overview
Input MPI program
Performance Stats Collection
Path Construction
Performance Visualization
Output graphs

## Slide 19: Performance Visualization
Idea is to identify messages that took the most amount of time
Identify a pattern among the messages, e.g. all the slow messages happened in a small time window
Identify patterns for e.g. the slow messages were due to a bottleneck in a particular component
Notes: It permits the coarse-grained study of distributed-memory applications.
For large, system-level experiments with thousands of network endpoints, high-accuracy cycle-accurate simulation is not possible, or at least not convenient. Simulation requires coarse-grained approximations to be practical.

## Slide 20: Heatmaps
Messages from node 80 and above appear darker; taken the most amount of time

## Slide 21: Per-component Bar Graphs
The most time is spent in Switch 21 for all graphs

## Slide 22: Conclusion and Future Work
Light-weight network monitoring is essential to provide deeper insights in to performance problems
Solution: protocol extensions, hardware extensions and software solutions to provide deeper insights into performance problems
Designed and prototyped an extendable performance analysis framework with broad applicability
Todos:
  Tie CPU-side calling context for source attribution
  Collect detailed component level metrics (queue length, arbitration)
  Evaluate on real-world large-scale applications
  Incorporate into PathForward/GenZ switch and bridge ASICs